## Slide 1: Test of PID control on the 9-reservoir grid network
Guilhem Mariotte
12/06/2020

## Slide 2: Reservoir network configuration
Reservoirs adjacent by their N-S-E-W faces, no trips in diagonal (like R1 to R5)
Two border nodes by reservoir border: one for each flow direction (eg, node 49 = R2 to R5, node 50 = R5 to R2)

## Slide 3: Demand scenario (reference scenario)
Internal origin and destination nodes are not used, only external entry and exit nodes
No internal trips, only trips crossing the whole network. 32 macro routes in total (succession of nodes)

## Slide 4: MFD fit from Symuvia outputs

## Slide 5: Comparison with Symuvia outputs

## Slide 6
Good match for accumulation evolution, less accurate for mean speed evolution
Two models can be used for the MFD simulation: accumulation-based or trip-based. Although slightly better results are obtained with the trip-based one, only the accumulation-based model will be used then as it is much faster to compute (a few seconds vs a few minutes for the trip-based)

## Slide 7: PID control for the 4 nodes to enter R5
Setpoint = 1000 veh (critical accumulation of R5)
Kp = 0.008
Ki = 0
Kd = 0

## Slide 8: PID control for the 4 nodes to enter R5

## Slide 9: PID control for the 4 nodes to enter R5
The node max flow given by the controler is shown in light gray

## Slide 10: PID control for the 4 nodes to enter R5
Improve the traffic conditions in R5, but worsen the conditions in R2, R4, R6 and R8. For the whole network, worse conditions.